The cosmic radiation at microwave frequencies varies with frequency as

(1)

which has an average of 2.78 K for the 20-32 Ghz range.

Ocean permittivity is complex with real and imaginary parts

(2)

and

(3)

so total permittivity is defined as,

Figure 3.11 The modified and nominal ocean dielectric permittivity models, ModKS and KS77(in pink) and ModE and E96 (in blue).  The plots show the variation in both the real and imaginary parts of the permittivity versus frequency.  The error bars denote the standard deviations in the modified models.  All plots are for Tsea=280K and S= 35‰.  Use Mod E.

FORTRAN subroutines:

* Gaussian subroutine returns a zero mean, sigma standard deviation, gaussian realization

FUNCTION GAUSSIAN(SIGMA)

REAL GAUSSIAN,SIGMA

GAUSSIAN = (-2.0*LOG(RAND() + 1.0E-20))**0.5*SIGMA*

1   COS(3.141592654*RAND())

RETURN

END

*subroutine to compute Tdownwelling where ka= water + oxygen attenuations

* Begin computation of radiative transfer integral

*Integration of Tb_dn, Tb_up, opacity.

DO 45 ifr = 1 ,3

freq =fre(ifr)

**	    Compute  the DOWNWELLING BRIGHTNESS TEMPERATURE	*********

TBdn(ifr) = 0.

opa = 0.0

TAU = 1.0

cloudflag = 0

DO 130 J = 1, JJ

vap =v(j)

pre =p(j)

tem =t(j)

absorp=	VAPOR(freq,Vap,Pre,Tem,CL,CW,CC)+

1		OXYGEN(freq,Vap,Pre,Tem,CX)

LTMP0 = EXP(-DZ*absorp)

DTB = Tem*(1.0 - LTMP0)*TAU

TAU = TAU*LTMP0

TBdn(ifr) = TBdn(ifr) + DTB

130	 CONTINUE

tauf(ifr) = tau

* Add on freq dependent cosmic background term:

TBdn(ifr) = TBdn(ifr) + (2.757+0.00379*(freq-18))*TAU

*

*COMPUTE THE  UpWELLING BRIGHTNESS TEMPERATURE***********

TBup(ifr) = 0.

TAU = 1.0

DO 135 J =  JJ,1,-1

vap =v(j)

pre =p(j)

tem =t(j)

LTMP0 = EXP(-DZ*(VAPOR(freq,Vap,Pre,Tem,CL,CW,CC)+

1		OXYGEN(freq,Vap,Pre,Tem,CX)	) )

DTB = Tem*(1.0 - LTMP0)*TAU

TAU = TAU*LTMP0

TBup(ifr) = TBup(ifr) + DTB

135    CONTINUE

45	CONTINUE

Esta subrutina calcula la distancia entre 2 puntos dados en latitud/longitud

function spheredist(lat1,lat2,diff_lon )

*Returns the distance in km between 2 points

*given by the lat/lon coordinates.

*Input lat at both points and difference in longitude values.

*Assumes a spherical Earth of radius 6367.6 km.

real lat1,lat2,diff_lon

term1=cos(lat1)*cos(lat2)*cos(diff_lon)

term2 = sin(lat1)*sin(lat2)

suma=term2+term1

if ( suma>=1.0 .and. suma<1.1)THEN

SPHEREDIST=0.0

GOTO 33

END IF

*	PRINT *,SUMA,LAT1,LAT2,DIFF_LON

spheredist= 6367.6*acos(SUMA)

33	return

end

*Radiative Transfer Equation For Down Lookin Radiometer.

DO IDAT = 1,209

*	print *,'tsurf=',tsurf-273.14,' tsea=',tsea(IDAT)

TS= TSEA(IDAT)

S=SAL(IDAT)

sig= sig0 (idat)

DO IFRE= 1,3

irow = irow + 1

F=FRE(IFRE)

TC = 2.757 + 0.00379 *(F-18)

PER = PERMITIVITY(TS, S,f)

E_spec= 1+ abs( (1-sqrt(per))/(1+sqrt(per)) )

w= wind(sig)

emiss= E_spec * es0 + ew0*w

e_t = exp(-tau(ifre,idat))

Tbest0(irow) = Tu(ifre,idat) + e_t*

1 ( emiss*Ts + (1-emiss)*(td(ifre,idat) +tc* e_t) )

END DO

* Header format for NWS radiosonde data files

9	READ (12,3, IOSTAT=EOF ) wmo(i),lat(i),lon(i),ele(i),year(i),mo(i)

2	,da(i),hr(i),lvl(i),q(i),press(i),height(i),temp(i),relhm(i)

2	,dpdp(i),wndsp(i),dir(i),lt(i), et(i),p(i),h(i),t(i),u(i),dp(i)

2	,wd(i)

IF(EOF.GE.0)THEN

IF (lvl(i) .LE. 1) THEN

READ (12,4) heWMO,heLAT,heLON,heELEV,heYEAR,heMO,heDA,heHR

2    ,heLVL,heQ,hePRESS,heHEIGHT,heTEMP,heRELHM,heDPDP,heWNDSP

2    ,heDIR,heLT,heET,heP,heH,heT,heU,heDP,heWD

READ (12,2) heN1,heD1,heD2,heM1,heN2,heMB,heM2,heC1,hePC,heC2

2	,heMS