## Slide 1: DAC Characterization

## Slide 2: Calculating Best Line Fit
Setting initial values C program
Double k1=0; k2=0; k3=0; k4=0;
int i;
float Gain, Offset, Sample[NSAMPLES], Best_Fit_Line[NSAMPLES];
collect_DAC_Samples(sample)/*measures and Stores DAC output voltages*/
for (i=0;i<NSAMPLES;i++)
{ k1=k1+I; k2=k2+Sample[i];k3=k3+i2;k4=k4+i*Sample;}
Gain=(NSAMPLES*k4-k1*k2)/(NSAMPLES*k3-k12);
Offset=k2/NSAMPLES-Gain*(k1/NSAMPLES);
for(i=0;i<NSAMPLES;i++)
Best_fit_line[i]=Gain*i+Offset;

## Slide 3: Table for calculation
Excel table for calculation 11.1-11.2
  Best Fitted line
  Gain error %=100*(Actual Gain/Ideal Gain-1)
  Ideal line for abs max error calculation

## Slide 4: Experimental Best Fitted Line and Ideal
Chart: 
| -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
vout | -780 | -705 | -530 | -455 | -400 | -325 | -150 | -75 | 120 | 195 | 370 | 445 | 500 | 575 | 750 | 825
BFL | -797.8529 | -688.4558 | -579.0587 | -469.6616 | -360.2645 | -250.8674 | -141.4703 | -32.0732 | 77.3239 | 186.721 | 296.1181 | 405.5152 | 514.9123 | 624.3094 | 733.7065 | 843.1036
Ideal | -800 | -700 | -600 | -500 | -400 | -300 | -200 | -100 | 0 | 100 | 200 | 300 | 400 | 500 | 600 | 700

## Slide 5: DAC Absolute Error LSB
Chart: 
| -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
DAC Abs Error (LSB) | 0.2 | -0.05 | 0.7 | 0.45 | 0 | -0.25 | 0.5 | 0.25 | 1.2 | 0.95 | 1.7 | 1.45 | 1 | 0.75 | 1.5 | 1.25

## Slide 6: Monotonicity
Chart: Monotonicity
| -8 | -7 | -6 | -5 | -4 | -3 | -2 | -1 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
vout | -780 | -705 | -530 | -455 | -400 | -325 | -150 | -75 | 120 | 195 | 370 | 445 | 500 | 575 | 750 | 825

## Slide 7: Differential non Linearity (DNL)
The curve is monotonic but not uniform (see graph)
Ideal step is LSB=100mV
Differential non linearity is a figure of merit that describes the uniformity of the step size in the DAC code.
DNL represents the error in each step size represented in LSB fractions

## Slide 8: DNL Calculation
Take 1st derivative values
Calculate average LSB size=109.35mV using best fit line calculation which equals the gain calculated with Best fitted line.
Divide each step by average LSB
1st derivative | dnl ERROR
75 | 0.688073
175 | 1.605505
75 | 0.688073
55 | 0.504587
75 | 0.688073
175 | 1.605505
75 | 0.688073
195 | 1.788991
75 | 0.688073
175 | 1.605505
75 | 0.688073
55 | 0.504587
75 | 0.688073
175 | 1.605505
75 | 0.688073