## Slide 1: Diminished Radii Complement and codes
INEL 4205

## Slide 2: Definition
Given a number N in base r having n digits, the (r - l)'s complement of N is defined as:
(r" - 1) - N.
For Decimal numbers
r = 10 and r - 1 = 9, so the 9's complement
of N is (10n - 1) - N.
Now, 10n represents a number that consists of a single 1
followed by n O's.
10" - I is a number represented by n 9's.

## Slide 3: Example for decimal numbers
For example, if n = 4,
we have 104 = 10,000 and
10000- 1 = 09999.
It follows that the 9's complement of a decimal number is obtained by subtracting each digit from 9.
The 9's complement of 546700 is 999999 - 546700 = 453299.
The 9's complement of 012398 is 999999 - 012398 = 987601.

## Slide 4: Example for binary numbers (r=2)
For example, if n = 4,
we have 104 = 10000
10000- 1 = 01111.
It follows that the 1'st complement of a binary number is obtained by subtracting each digit from 1.
The 1'st complement of 101010 is
  111111 - 101010 = 010101.
The 1'st complement of 001 is 111 - 001 = 110.

## Slide 5: Two’s Complement of Binary Number
Invert every number
Example: N=11001100
ones complement =00110011
two’s complement = one’s complement +1=00110100

## Slide 6: Subtracting using twos complement
Using 10's complement, subtract 72532 - 3250.
M= 72532
10' s complemen t of N = + 96750
Sum = 169282
Discard end carry 105 = -100000
Answer = 69282
•Note that M has 5 digits and N has only 4 digits. Both numbers must have the same number of digits; so we can write N as 03250.
Taking the lO's complement of N produces a 9 in the most significant position. The occurrence of the end carry signifies that
M >=N and the result is positive.

## Slide 7: Subtraction using 2’s complement with binary numbers
X = 1010100 and Y = 1000011,
X= 1010100
2's compY = + 0111101
Sum = 10010001
Discard end carry 2' = - 10000000
Answer: X - Y = 0010001
Y= 1000011
2's comp of X = + 0101100
Sum = 1101111
There is no end carry.
Answer:
Y - X = (2's comp of 1101111)
= -0010001 •
X-Y
Y-X

## Slide 8: ASCII Code
The ASCII code contains 94 graphic characters that
can be printed and 34 nonprinting characters used for various control functions. The graphic characters consist of the 26 uppercase letters (A through Z), the 26 lowercase letters (a through z), the 10 numerals (0 through 9), and 32 special printable characterssuch as %, *, and $.

## Slide 9: American Standard Code for Information Interchange (ASCII)

## Slide 10: American Standard Code for Information Interchange (ASCII)

## Slide 11: Registers
Group of binary cells
A cell stores one bit of information.
Register contains n cells therefore can store n bits of information.
The State of the register is an n-tuple number of 1’s and 0’s.
The content of a register is a function of the interpretation given to the information stored in it

## Slide 12: Register information
An interregister transfer operation – transfer of information from one register to another.
Information from keyboard if ASCII enters in the memory as an 8 bit register.
The eighth bit is a parity bit.
The 8 bits are stored in the LSBits of the register and later are shifted

## Slide 13: Transfer of information among registers

## Slide 14: FIGURE 1.2 Example of binary information processing

## Slide 15: Table 1.8 Truth Tables of Logical Operations

## Slide 16: FIGURE 1.3 Signal levels for binary logic values

## Slide 17: FIGURE 1.4 Symbols for digital logic circuits

## Slide 18: FIGURE 1.5 Input–output signals for gates

## Slide 19: FIGURE 1.6 Gates with multiple inputs