## Slide 1
Last Lecture – MOS Transistor Review (Chap. #3)
Transistor Operation Regions & Large Signal Behavior
  saturation - Vds>Vds(sat)
  ohmic - Vds<Vds(sat)
  subthreshold - Vds> 0.2V
Small Signal Model
  low-frequency model
  frequency dependent model (parasitic capacitances)
Single Stage Amplifiers
  voltage gain
  terminal impedances
Vsb effect!
Basic Design Exercises

## Slide 2
Single Stage Amplifiers

## Slide 3
Single Flow in Transistors
It is important to recognize that ac signals can only flow into and out of certain transistor terminals.
Rules:
  The drain can never be an input terminal.
  The gate can never be an output terminal.

## Slide 4
Transistor Design #1
Design the transistor’s W/L such that it operates in the saturation region for ID=10µA
ID
VG
where
  Kn=100µA/V2
Si VDSSAT=0.2V entonces W/L=5

## Slide 5
Transistor Design #2
Design the transistor’s W/L such that it operates in the saturation region for ID=10µA and VD = [0.5 - 3.1] V.
where
  Kp=100µA/V2
  VDD=3.3V
VDD
VG
ID
VD
Si VDSSAT min=3.3-3.1=0.2V
Entonces W/L=5

## Slide 6
Transistor Design #3
Design the transistor’s W/L such that it operates in the saturation region for ID=[0.1 – 10] µA and VX(max)=1.2V.
where
  Kn=100µA/V2
  Vt0=0.7V
ID
VX
This connection is a diode connection and ensures saturation

## Slide 7
Common Source Amplifier
Vin
VDD
Vout
M1
Ibias
VGS
ID
Simplified
Schematic
Vin
VDD
VB
Vout
M2
M1
Implementation

## Slide 8
Common Source Amplifier
Typical design approach:
  Id set by power constraints
  Vds1(sat) & Vds2(sat) set by output voltage range constraints if any
  hence (W/L)1 & (W/L)2
  3. (W/L)1 set by gain constraints (there might be a need for redesign M1)
Vin
VDD
VB
Vout
M2
M1
Large Signal Behavior
  Vout(min) – VDSSAT Typically VDSSAT0.2V
  Vout(max) –VDD-VSDSAT Typically VSDSAT0.2V
Small Signal Behavior
  Av – -gmRout : where Rout=ro2||ro1

## Slide 9
Common Source Amplifier
Design the following CS amplifier for the following specifications:
  Vout = [0.15 – 2.7] V
  Psupply < 90μW
  |Av| > 30 V/V
where
  VT0n=|VT0p|=1.0V
  K’n=100µA/V2
  K’p=25µA/V2
  λn= λp =0.2V-1
  VDD=3.0V
Vout
VDD
Vin
Iref
=10µA
VDD
M2
M1
M3