## Slide 1: Review problems
Exam 1

## Slide 2: Problem 1
For the following circuit, specify the required values of VDD, RD and W=L such that:
high and low output voltages equal to VOH = 2V and VOL = 0.1V , respectively, are obtained, and so that the current drain from the supply in the low-output state is 20mA.
The transistor has
Vt = 0.5V and unCox = 100A/V2

## Slide 3: Problem 2
The pull-down (PD) network for a complex CMOS gate is shown below. Determine
(i) the logic function,
(ii) the graph diagram that correspond to the PD network,
(iii) the graph diagram that correspond to the pull-up network needed to implement the logic function, and
(iv) the (W=L) ratios for all NMOS and PMOS transistors if the circuit is based on the reference inverter with
(W/L)n = 2/1 and (W=L)p = 5/1.

## Slide 4: Problem 3
Consider a matched CMOS inverter fabricated in the 0.13um process for which
Vtn=-Vtp = 0.5V, VDD = 1.8V, upCox=unCox=300uA/V2.
If the load capacitance C = 20fF, use the method of average currents to determine the required (W/L) ratios so that tp=20ps.