## Slide 1
Digital Logic Inverter
Clasificacion de Circuitos y frecuencia maxima

## Slide 2
The Voltage-Transfer Characteristic (VTC)
The function of the inverter is to invert the logic value of its input signal
The voltage-transfer characteristic is used to evaluate the quality of inverter operation
VTC parameters
  VOH: output high level
  VOL: output low level
  VIH: the minimum value of input interpreted by the inverter as a logic 1
  VIL: the maximum value of input interpreted by the inverter as a logic 0
  Transition region: input level between VIL and VIH

## Slide 3
Noise Margins
The VTC is generally non-linear
VIH and VIL are defined as the points at which the slope of the VTC is =-1
Robustness (noise margin at a high level): NMH = VOH - VIH
Robustness (noise margin at a low level): NML = VIL - VOL
Static inverter characteristics for ideal VTC:
  VOH = VDD
  VOL = 0
  VIH = VIL = VDD/2
  NMH = NML = VDD/2

## Slide 4
Dynamic power dissipation: power dissipated as the output is switching
Static power dissipation: power dissipated when the inverter stays in logic 0 or logic 1
Power Dissipation

## Slide 5: Propagation Delay
tPHL : high-to-low propagation delay
tPLH : low-to-high propagation delay
tP (propagation delay) = (tPLH + tPHL)/2
Maximum switching frequency fmax = 1/(2tP)
The transient of the inverter can be characterized by a RC charge/discharge model